## Slide 1: FTC Library
Michael Tsang
8/15/2012

## Slide 2: Agenda
Background on multi-tasking.
Introducing the FTC templates.
Introducing the FTC library.
  Input modules
  Output modules
  Miscellaneous modules
Coding Exercises:
  Do arcade drive with joystick.
  Control various appendages using joystick/gamepad.
  Using PID control to move an appendage smoothly.
  Autonomously drive the robot using time (i.e. dead reckoning).
  Autonomously drive the robot using sensors and PID control (e.g. encoders, gyro, sonar, light etc).
  Monitor battery voltages using the battery module.
  Add code to use the menu module to provide competition options.

## Slide 3: Typical RobotC Program
task main() { RobotInit(); while (true) { if (sensor1 has a certain value) { // do something to react to the sensor } else if (sensor1 has other values) { // do something else to react to the sensor } else { // do something else }
if (sensor2 have some values)
{
//do something to react to those sensors.
}
… wait1Msec(100); } }

## Slide 4: Problems with Typical RobotC Program
One single task, so it will be doing only one thing at a time.
If an operation does not complete immediately, the code may need to wait by polling. When the code is polling, nothing else can be done.
Robot needs to handle multiple events as they happen. For example, while the robot is being driven forward with joystick, a button may be pressed to operate a claw to open and close while the robot is still moving. With the typical code, the robot cannot respond to joystick changes while operating the claw.

## Slide 5: Typical Program Example
task main() { while (true) { if (joystick forward) // program wheel motor forward else if (joystick backward) // program wheel motor backward else // stop the wheel motors
while (joystick button 1 is pressed)
if (claw is not fully opened) // program claw motor to open else
// program claw motor to stop
//program claw motor to stop
wait1Msec(100);
}
}

## Slide 6: Improving Typical Program
task main() { while (true) { if (joystick forward) // program wheel motor forward else if (joystick backward) // program wheel motor backward else // stop the wheel motors
if (joystick button 1 is pressed and claw is not fully opened)
// program claw motor to open else
// program claw motor to stop
wait1Msec(100);
}
}

## Slide 7: Introducing the Task Concept
void DriveTask()
{
if (joystick forward) //input // program wheel motor forward (output) else if (joystick backward) //input // program wheel motor backward (output) else // stop the wheel motors (output)
}
void ClawTask() {
if (joystick button 1 is pressed and claw is not fully opened) //input
// program claw motor to open (output) else
// program claw motor to stop (output)
}
task main() { while (true) { DriveTask();
ClawTask(); wait1Msec(100);
}
}

## Slide 8: Real Life Example of Multitasking
Baking a pizza - here are the steps:
  Preheat oven to 350 degree-F
  Wait for the oven to reach preheat temperature
  Put pizza in the oven, set timer for 20 min.
  Wait for timer to go off.
  Turn off oven, take pizza out and serve.
Doing laundry – here are the steps:
  Put clothes into washer, put in detergent and softener. Start washer.
  Wait for the washer to stop.
  Transfer clothes to the dryer and start the dryer.
  Wait for the dryer to stop.
  Take clothes out of the dryer, fold them and put them away.

## Slide 9: Real Life Multitasking Example (cont)
task main() { while (true) { PizzaTask();
LaundryTask(); wait1Msec(100);
}
}
void PizzaTask()
{
static int step = 0;
switch (step) {
case 0: {
Preheat oven to 350 degreeF;
step++;
break;
}
case 1: {
if (oven temperature >= 350) step++;
break;
}
case 2: {
Put pizza in the oven;
set timer to 20 min;
step++;
break;
}
case 3: {
if (timer >= 20 min) step++;
break;
}
case 4: {
Take pizza out of the oven and serve;
step++;
break;
}
default: break;
}
}
void LaundryTask()
{
static int step = 0;
switch (step) {
case 0: {
Put clothes in washer;
Put in detergent and softener;
Start washer;
step++;
break;
}
case 1: {
if (washer stopped) step++;
break;
}
case 2: {
Transfer clothes to the dryer;
Start dryer;
step++;
break;
}
case 3: {
if (dryer stopped) step++;
break;
}
case 4: {
Take clothes out, fold them and put away;
step++;
break;
}
default: break;
}
}

## Slide 10: Introducing the FTC Library Main Task Template
task main()
{
long nextPeriod;
RobotInit();
nextPeriod = nPgmTime;
while (true) {
HiFreqTasks();
if (nPgmTime >= nextPeriod) {
nextPeriod += PERIOD_INTERVAL; InputTasks();
MainTasks();
OutputTasks();
}
EndTimeSlice();
}
}

## Slide 11: Using the FTC Library Main Template
void InputTasks()
{
getJoystickSettings(joystick);
g_clawPos = nMotorEncoder[clawMotor];
}
void MainTasks()
{
// DriveTask
g_drivePower = joystick.joy1_y1;
// ClawTask
g_clawPower = (joy1Btn(1) && (g_clawPos < FULLY_OPENED))? 50: 0;
}
void OutputTasks()
{
// Drive Task
motor[leftMotor] = g_drivePower;
motor[rightMotor] = g_drivePower;
// Claw Task
motor[clawMotor] = g_clawPower;
}

## Slide 12: FTC Library Modules
All library modules are organized as objects.
To use a module:
  Include the header file of the module in your main program.
  Create an object by declaring a global variable with the object type in your main program.
  Initialize the object by calling its xxxInit() function in your RobotInit(), providing parameters if necessary.
  If the module has a periodic task, call it.
    For sensor modules, call its xxxTask() function in your InputTasks().
    For actuators, call its xxxTask() function in your OutputTasks().
  If the module requires Callback handlers, provide the required xxxEvent() function even if there is nothing to do.
  If necessary, you can call any provided functions of the modules.

## Slide 13: Input Modules
Sensors
  Touch.h: Touch sensor
  Gyro.h: Gyro sensor
  Accel.h: Accelerometer
  Analog.h: Miscellaneous analog sensors that need zero-offset/deadband calibration
  Sensor.h: Analog sensors used as event sensors
  IRSeeker.h: Infrared sensors
  Radar.h: Ultrasonic sensor on a rotating platform
Human Input Devices (HID)
  JoyBtn.h: Joystick buttons
  NxtBtn.h: NXT Mindstorms buttons

## Slide 14: Output Modules:
Servo.h: Servo motors with limit switch support
Drive.h: Robot drive (Tank, Arcade, Mecanum)
PIDCtrl.h: Generic PID controller
PIDDrive.h: PID controlled drive
PIDMotor.h: PID controlled motor
LnFollow.h: Line follower
WallFollow.h: Wall follower

## Slide 15: Miscellaneous Modules:
SM.h: Generic State Machine support
Timer.h: Generic timer
Batt.h: Battery status support
Menu.h: Menu support for user input

## Slide 16: Module: Touch.h
TouchInit(): Initialize the touch sensor specifying the sensor ID and options.
TouchEvent(): Must provide this callback for notifying touch sensor triggers.
TouchTask(): Must be called in your InputTasks().

## Slide 17: Module: Gyro.h
GyroInit(): Initialize the gyro sensor and do zero/deadband calibration.
GyroReset(): Call this function to reset the gyro heading data.
GyroGetTurnRate(): Return the gyro turn rate value.
GyroGetHeading(): Return the integrated heading value.
GyroTask(): Must be called in your HiFreqTasks() for integrating the heading value.

## Slide 18: Module: Accel.h
AccelInit(): Initialize the accelerometer and do zero/deadband calibration.
AccelReset(): Clear all the internal accelerometer data.
AccelGetXYZAccel(): Returns the acceleration value of the X, Y or Z axes.
AccelGetXYZVel(): Returns the velocity value of the X, Y or Z axes.
AccelGetXYZDist(): Returns the distance value of the X, Y or Z axes.
AccelSetEnable(): To enable or disable the accelerometer.
AccelTask(): Must be called in your HiFreqTasks().

## Slide 19: Module: Analog.h
AnalogInit(): Initialize the analog sensor and do zero/deadband calibration.
AnalogSetCalibration(): Manually set the calibration value.
AnalogReadValue(): Read the analog sensor value and apply zero offset and deadband to the value.

## Slide 20: Module: Sensor.h
SensorInit(): Initialize the module specifying the low and high thresholds and options.
SensorCal(): Call this function to start and stop calibration to determine the thresholds.
SensorEvent(): Must provide this callback for notifying sensor events when the sensor value crosses the thresholds.
SensorTask(): Must be called in your InputTasks().

## Slide 21: Module: IRSeeker.h
IRSeekerInit(): Initialize the IRSeeker sensor and options.
IRSeekerGetACDir(): Return the direction value of the IR Beacon.

## Slide 22: Module: Radar
RadarInit(): Initialize the module and specifying the sonar sensor, the radar motor and other parameters.
RadarAddSample(): Call this function to add a radar sampling point at the given angle.
RadarGetData(): Return the radar value of the given radar angle.
RadarSetEnable(): Call this function to enable or disable the radar.
RadarTask(): Must be called in your InputTasks().

## Slide 23: Module: JoyBtn.h
JoyBtnInit(): Initialize the module and the initial joystick button values.
JoyBtnEvent(): Must provide this callback function for notifying button events.
JoyBtnTask(): Must be called in your InputTasks().

## Slide 24: Module: NxtBtn.h
NxtBtnInit(): Initialize the module and the initial NXT button values.
NxtBtnEvent(): Must provide this callback function for notifying NXT button events.
NxtBtnTask(): Must be called in your InputTasks().

## Slide 25: Module: Servo.h
ServoInit(): Initialize the Servo module. There are two variations, one for angle servo, one for continuous servo and optionally specifying limiting switch IDs.
ServoGetAngle(): Call this function to get the target angle of the servo.
ServoSetAngle(): Call this function to set the target angle of the servo.
ServoContinuousSetSpeed(): Call this function to set the speed of the continuous servo.
ServoTask(): Must be called in your OutputTasks().

## Slide 26: Module: Drive.h
DriveInit(): Initialize the drive system by specifying the left and right motors (for 2-wheel drive), the rear left and right motors (for 4-wheel drive) and the drive options.
DriveStop(): Call this function to stop the drive system.
DriveReset(): Call this function to stop the drive system as well as resetting the drive stalled states.
DriveStallProtect(): Enable or disable the drive stall protection.
DriveArcade(): Call this function to do arcade drive.
DriveMecanumCartesian(): Call this function to do mecanum drive providing Cartesian info (X, Y and Rotation).
DriveMecanumPolar(): Call this function to do mecanum drive providing Polar info (Magnitude, Direction and Rotation).
DriveEvent(): Must provide this callback function for notifying completion of drive operation.
DriveTask(): Must be called in your OutputTasks().

## Slide 27: Module: PIDCtrl.h
PIDCtrlInit(): Initialize the PID controller providing all the PID control parameters.
PIDCtrlReset(): Call this function to reset the PID controller.
PIDCtrlGetError(): Return the last error (e.g. distance to target).
PIDCtrlSetPowerLimit(): Call this function to set the PID output power limits.
PIDCtrlSetTarget(): Call this function to set the target value and start the PID controller.
PIDCtrlIsOnTarget(): Call this function to determine whether the PID controller has reached target.
PIDCtrlOutput(): Call this function to calculate the PID control output providing the current input.
PIDCtrlGetInput(): Must provide this callback function for reading the current input value.

## Slide 28: Module: PIDDrive.h
PIDDriveInit(): Initialize the PIDDrive module providing the Drive subsystem, the PID controllers and specifying the options.
PIDDriveReset(): Call this function to cancel the PID drive started by a PIDDriveSetTarget.
PIDDriveSetTarget(): Call this function to set the PID drive targets and start the PID controllers. There are two variations, one for 4-wheel macanum drive, one for 2-wheel arcade drive.
PIDDriveEvent(): Must provide this callback for notifying the completion of PIDDriveSetTarget.
PIDDriveTask(): Must be called in your OutputTasks().

## Slide 29: Module: PIDMotor.h
PIDMotorInit(): Initialize the PIDMotor module providing the motor ID, the PID controller and specifying the options.
PIDMotorReset(): Call this function to stop the motor and cancel the PID controller.
PIDMotorSetPower(): Call this function to set the direct motor power and cancel the PID controller if necessary.
PIDMotorSetTarget(): Call this function to set the PID motor targets and start the PID controller.
PIDMotorEvent(): Must provide this callback for notifying the completion of PIDMotorSetTarget.
PIDMotorTask(): Must be called in your OutputTasks().

## Slide 30: Module: LnFollow.h
LnFollowInit(): Initialize the Line Follower module and specifying the drive system and the PID controller.
LnFollowStart(): Call this function to start line following providing the stopping condition, the maximum drive power when following the line, the strategy of finding the line and the timeout value.
LnFollowStop(): Call this function to stop the line follower.
LnFollowSetFindPower(): Call this function to set the strategy and power of finding the line.
LnFollowTask(): Must be called in your OutputTasks().

## Slide 31: Module: WallFollow.h
WallFollowInit(): Initialize the Wall Follower module and specifying the drive system and the PID controllers.
WallFollowStart(): Call this function to start wall following providing the distance from the wall, the drive power and the driving pattern when looking for a wall.
WallFollowStop(): Call this function to stop the wall follower.
WallFollowSetFindPower(): Call this function to set the strategy and power of finding the wall.
WallFollowTask(): Must be called in your OutputTasks().

## Slide 32: Module: SM.h
SMInit(): Initialize the state machine.
SMStart(): Call this function to start the state machine and optionally specifying the starting state.
SMStop(): Call this function to stop the state machine.
SMIsReady(): Call this function to determine if the state machine is in ready state.
SMAddWaitEvent(): Call this function to add an event to wait for.
SMWaitEvents(): Call this function to put the state machine into wait state waiting for the added events.
SMSetEvent(): Call this function to trigger the event that state machine is waiting for when something happened.

## Slide 33: Module: Timer.h
TimerInit(): Initialize the timer and specify the options.
TimerSet(): Call this function to set the timeout value and start the timer.
TimerReset(): Call this function to cancel and reset the timer.
TimerEvent(): Must provide this callback for notifying timeout event.
TimerTask(): Must be called in your InputTasks().

## Slide 34: Module: Batt.h
BattInit(): Initialize the module to monitor the battery voltages and specify how battery info is displayed on the LCD screen.
BattSetState(): Enable/Disable of battery info on the LCD screen.
BattTask(): Must be called in your OutputTasks().

## Slide 35: Module: Menu.h
MenuInit(): Initialize the LCD choice menu specifying the menu title.
MenuAddChoice(): Call this function to add a choice to the menu.
MenuSetState(): Call this function to enable or disable the menu. Enabling the menu will cause it to be displayed on the LCD screen.
MenuGetChoice(): Call this function to enable menu and get the user’s choice. This function waits until the user makes a choice.

## Slide 36: Resources
This slide deck is available on http://proj.titanrobotics.net/docs/Classes
Source code to the library can be found on http://proj.titanrobotics.net/hg/Ftc/<year>/code under files/ftclib
Source code to the competition code of various years can be found on http://proj.titanrobotics.net/hg/Ftc/<year>/code